## Slide 1: Presentation of a database management system to handle instruments and measurements
30. September 2021 | Forschungszentrum Jülich GmbH
Institute of Energy and Climate Research – IEK 8 (Troposhere)
M. Kennert, U. Bundke, A. Gomes, C. Mahnke, S. Rohs, A. Petzold

## Slide 2: outline
Database
05
06
07
Create an Instrument
Create a Calibration
Deploy an Instrument
Import a Time Series
08
Workflow
09
10
11
Overview
Import your Data
QA/QC Framework
12
Export your Data
System Overview
01
02
Our Mission
IAGOS Workflow
03
Our Solution
04
System Setup
System Overview
Database
Workflow
30. September 2021 │ Slide 1 of 19

## Slide 3: Our mission
European Research Infrastructure since 2014 (historical MOZAIC: 1994 - 2014)
Regular in-situ monitoring of essential climate variables H2O, O3, CO, NOx, CO2, CH4, aerosols, clouds
7 long-haul aircraft (IAGOS-CORE) + 1 Flying Laboratory (IAGOS-CARIBIC)
Provision of data in near real time for Copernicus and other service
28 June 2021: 62617 flights in database
O3
H2O
CO
NOx
CO2
CH4
IAGOS-CORE
aerosol
clouds
System Overview
Database
Workflow
30. September 2021 │ Slide 2 of 19

## Slide 4: IAGOS WORKFLOW
IAGOS Data Centre
hosted by AERIS
in Toulouse, France
deployment maintenance
data
calibration data
meta data
near real time
data transfer
IAGOS data products
Research Institutions
System Overview
Database
Workflow
30. September 2021 │ Slide 3 of 19

## Slide 5: Our solution
External B
30. September 2021 │ Slide 4 of 19
System Overview
Database
Workflow
Users
FZJ Data Portal
Systems
Storage
Raw Files
Reports
Instruments
Deployments
Time Series
Volume
Database
External A
External C
Technicians
Scientists
PIs
System
External
System properties
Realized with Docker
Application is implemented with Python and Django
Supports common databases (e.g., PostgreSQL )
Interaction via Web Browser or REST-API
Includes a configurable Workflow system
Provides algorithms for QA/QC checks
Provides JupyterHub-Service
Adaptable to other projects
Web Browser or REST-API
Machine-to-Machine
Communication
(FTP, REST, etc.)

## Slide 6: User interaction
FZJ Data Portal
System Overview
Database
Workflow
JupyterHub
Use the REST-API to produce customized quicklooks
Simple and intuitive web interface to manage the data
30. September 2021 │ Slide 5 of 19
+

## Slide 7: Advantages of using the portal
Centralized
Traceable
Compatibility
Problem
Groups usually have the data stored at different locations. For example, files are stored in separate folders or systems
Advantage
Portal will centralize the data and make it accessible
Portal will also provide filters to search for specific data
Problem
It‘s often too difficult to overview the whole measurement process
It‘s often not clear which data was used for calculations
Advantage
Stores every information (deployment, setup, calibrations)
Stores the relation between the series to make data reconstructable
Problem
Groups usually have the data stored in different structures and formats
It is hard to share the data since the structures are not compatible
Advantage
All groups have the same database structure and the same models
Data and implemented components can be easily shared
System Overview
Database
Workflow
30. September 2021 │ Slide 6 of 19

## Slide 8: Setup requirements
make
Conda is an open-source package management system for Python
Allows you to create multiple Virtual Environments to avoid dependency conflicts
Docker is an open platform for developing, shipping, and running applications
Allows you to deploy your system easily and ensures that your system is easy to scale up
Git is a free open source distrubuted version control system
We use Git to manage the code and to make it accessible
Make is a build automation tool
We use Make to avoid writing complicated shell commands and to build automated processes
System Overview
Database
Workflow
30. September 2021 │ Slide 7 of 19

## Slide 9: System Setup
Install the needed Python packages
Run the web application (Django)
Run the docker system (optional)
Download code from repository
Production System
Configure the Production System
setup instructions
Create a Virtual Environment
System Overview
Database
Workflow
30. September 2021 │ Slide 8 of 19

## Slide 10: Create an instrument
ICH Unit
HumiCap
RH Sensor
PT100 Sensor
Transmitterbox
IAGOS CAPACITIVE HYGROMETER
ABSTRACT STRUCTURE
STEPS TO CREATE AN INSTRUMENT
Create component types
Assign parameters
Create Components
Create component classes
Build the Instrument
Metadata
Instance
INSTRUMENT
System Overview
Database
Workflow
30. September 2021 │ Slide 9 of 19

## Slide 11: Create an instrument
Unit
Unit
Sensor
Sensor
CPU
IAGOS CAPACITIVE HYGROMETER
ABSTRACT STRUCTURE
STEPS TO CREATE AN INSTRUMENT
Create component types
Assign parameters
Create Components
Create component classes
Build the Instrument
Metadata
Instance
INSTRUMENT
System Overview
Database
Workflow
30. September 2021 │ Slide 9 of 19

## Slide 12: Create an instrument
ICH Unit
HumiCap
RH Sensor
PT100 Sensor
Transmitterbox
IAGOS CAPACITIVE HYGROMETER
ABSTRACT STRUCTURE
STEPS TO CREATE AN INSTRUMENT
Create component types
Assign parameters
Create Components
Create component classes
Build the Instrument
Metadata
Instance
INSTRUMENT
System Overview
Database
Workflow
30. September 2021 │ Slide 9 of 19

## Slide 13: Create an instrument
H2O
Relative humidity
Temperature
IAGOS CAPACITIVE HYGROMETER
ABSTRACT STRUCTURE
STEPS TO CREATE AN INSTRUMENT
Create component types
Assign parameters
Create Components
Create component classes
Build the Instrument
Metadata
Instance
INSTRUMENT
System Overview
Database
Workflow
30. September 2021 │ Slide 9 of 19

## Slide 14: Create an instrument
SN-MKX27
SN-AGY34
SN-UBZ55
SN-APQ56
SN-CMP32
IAGOS CAPACITIVE HYGROMETER
ABSTRACT STRUCTURE
STEPS TO CREATE AN INSTRUMENT
Create component types
Assign parameters
Create Components
Create component classes
Build the Instrument
Metadata
Instance
INSTRUMENT
System Overview
Database
Workflow
30. September 2021 │ Slide 9 of 19

## Slide 15: Create an instrument
ICH Unit
HumiCap
RH Sensor
PT100 Sensor
Transmitterbox
IAGOS CAPACITIVE HYGROMETER
ABSTRACT STRUCTURE
STEPS TO CREATE AN INSTRUMENT
Create component types
Assign parameters
Create Components
Create component classes
Build the Instrument
Metadata
Instance
INSTRUMENT
System Overview
Database
Workflow
30. September 2021 │ Slide 9 of 19

## Slide 16: Create a Calibration
Create calibrations
Assign calibration parameters
Create parameters
Parameter | Pre-Cal | Post-Cal | Component
A | 42 | 40.5 | ICH Unit
B | 666 | 642 | ICH Unit
Timestamp | 2019-12-24 | 2022-01-06 | 
Name | Long Name | Unit | CF
A | - | ppm | -
B | - | ppm | -
1. Define the parameter
2. Define the calibrations
SAMPLE CALIBRATION
STEPS TO CREATE A CALIBRATION
Create a component
System Overview
Database
Workflow
30. September 2021 │ Slide 10 of 19
IAGOS CAPACITIVE HYGROMETER
INSTRUMENT

## Slide 17: Deploy an instrument
Create a location
Deploy your instrument
Create an instrument
Create a project
STEPS TO CREATE A DEPLOYMENT
PROPERTIES
Instrument Details
Location (Aircraft or Station)
Installation Timestamp
Removal Timestamp
Project Details
System Overview
Database
Workflow
30. September 2021 │ Slide 11 of 19

## Slide 18: Import a time series
TIME SERIES
Metadata
Levels, validities and revision
Instrument information
Deployment information
Relations
Calibrations
Calibration Functions
Time Series
STEPS TO CREATE A SERIES
Create data validities
Create the metadata of the
time series
Create data levels
Import data points
Create relations
System Overview
Database
Workflow
30. September 2021 │ Slide 12 of 19

## Slide 19: Workflow – overview
T2
T3
T1
T2
T3
Scheduler
Queue
hourly, daily, weekly
Metadata
Series
Waiting
Job 2
Series
Job 1 depends on Job 2
Process
Scheduler
Queue
hourly, daily, weekly
Job 1
Running
Job 2
Series
Metadata
Series
Job 1 depends on Job 2
Process
User
Job 1
Job 2
Metadata
Series
Series
QA/QC Tests
Job 1
System Overview
Database
Workflow
30. September 2021 │ Slide 13 of 19

## Slide 20: Task – overview
Import Manager
Parses and imports the data and process it afterwards
QA/QC Checks [In progress]
Checks the data. Flags it and creates a report for the PI
External Systems
Transfer Handler
Requests the data of the given source
Transfer Handler
Sends the data to the given destination
Reader
Importer
Export Manager
Writes the data into a specific format and exports the written data
External Systems
Writer
Exporter
Task
The PI checks the plausibility of the data. If the data is acceptable, the PI will release the data
Task manager
Reprocess
Transfer type
Authentication
Transfer type
Authentication
System Overview
Database
Workflow
30. September 2021 │ Slide 14 of 19

## Slide 21: Import your data
STEPS TO IMPORT YOUR DATA
Register your Reader
Implement an Importer
Implement a Reader
Register your Importer
Process Data
Import Data
Perform QA/QC tests
Interprete Data
External A
External C
Sources
Import Process
Transfer
Transfer
Transfer
Transfer
(Importer)
(Importer)
(Reader)
External D
External B
System Overview
Database
Workflow
30. September 2021 │ Slide 15 of 19

## Slide 22: QA/QC Framework – Autom8qc
Developed and used by the DE community
Application of probablistic approaches
Adaptable to different environments
Provides advanced QA/QC tests
OPEN SOURCE PROJECT
https://jugit.fz-juelich.de/m.kennert/autom8qc
OVERVIEW
TUTORIAL
https://autom8qc.readthedocs.io/en/latest
System Overview
Database
Workflow
30. September 2021 │ Slide 16 of 19

## Slide 23: QA/QC Framework – basic example
Perform Outlier Test
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Outlier
Before departure
After arrival
Too low values
Visualization
Execution Pipeline
QAQCTest
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
System Overview
Database
Workflow
30. September 2021 │ Slide 17 of 19

## Slide 24: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 25: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
Before departure
After arrival
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 26: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 27: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
Remove failed data points
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 28: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
Too low values
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 29: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 30: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
Remove failed data points
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 31: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
Outlier
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 32: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 33: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
Remove failed data points
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 34: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 35: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
If more than 40% of the data points have a probability
lower than 10% then set all probabilities to 0%
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 36: QA/QC Framework – basic example
Perform Rule
Map probabilities to validities
Perform Global Minimum Test
Perform Time Range Test
Merge results
Visualization
Execution Pipeline
QAQCTest
QAQCTest
BaseMeasure
BaseRule
BaseMapper
Data Points | Results | Test
2021-01-01 00:00:00 | Invalid | Time Range Test
2021-01-01 00:00:01 | Invalid | Time Range Test
2021-01-01 00:00:02 | Invalid | Time Range Test
… | … | …
2021-01-01 00:01:41 | Good | -
2021-01-01 00:01:42 | Good | -
… | … | …
2021-01-01 00:04:22 | Invalid | Global Minimum Test
… | … | …
2021-01-01 00:08:20 | Invalid | Outlier Test
… | … | …
2021-01-01 00:10:46 | Invalid | Global Minimum Test
2021-01-01 00:11:08 | Invalid | Global Minimum Test
… | … | …
2021-01-01 00:00:02 | Invalid | Time Range Test
System Overview
Database
Workflow
Perform Outlier Test
QAQCTest
30. September 2021 │ Slide 17 of 19

## Slide 37: Export your data
Register your Exporter
Implement a Writer
Implement an Exporter
Register your Writer
Prepare Data
Write Data
Read Data
External A
External C
Destination
Export Process
Transfer
Transfer
Transfer
Transfer
(Writer)
(Exporter)
(Exporter)
External D
External B
STEPS TO EXPORT YOUR DATA
System Overview
Database
Workflow
30. September 2021 │ Slide 18 of 19

## Slide 38: References
Repository – FZJ Instruments Database https://jugit.fz-juelich.de/m.kennert/instruments-db
Online Documentation – FZJ Instruments Database https://instruments-database.readthedocs.io/en/latest/index.html
FZJ Data Portal (FZJ Intranet) http://zam10200.zam.kfa-juelich.de/
Repository – QA/QC Framework https://jugit.fz-juelich.de/m.kennert/autom8qc
Online Documentation – QA/QC Framework https://autom8qc.readthedocs.io/en/latest/index.html
System Overview
Database
Workflow
30. September 2021 │ Slide 19 of 19